## Slide 1
LINUX KERNEL · I2C CAMERA SENSOR · EMBEDDED LINUX
Custom IMX219 Camera Driver
on Raspberry Pi
How sensor detection works, how the built-in driver claims the camera first, and how to bypass it cleanly to run your own.
Prepared by Karthikeya Dokku
IMX219 Custom Driver Bring-Up
1 / 15

## Slide 2
AGENDA
What We'll Cover
From boot-time detection to a fully validated custom driver
How Linux Detects the Camera
Device Tree parsing, I2C registration, and driver matching at boot
Internal Architecture of the Pi Camera Stack
From libcamera down through V4L2, the media controller, and the I2C bus
Why the Official Driver Wins by Default
Compatible-string matching and module load order favor the built-in driver
Three Ways to Bypass the Built-in Driver
Unload it, disable it, or rename it — choose the cleanest path for your case
Parameters Your Custom Driver Must Handle
Bring-up settings plus the runtime controls exposed by the IMX219
IMX219 Custom Driver Bring-Up
2 / 15

## Slide 3
BOOT-TIME DETECTION
How Linux Detects a Camera at Boot
Six steps happen before your driver ever gets a chance to run
Boot Sequence Starts
>
Device Tree Parsed
>
I2C Device Node Created
>
Compatible String Matched
>
probe() Function Called
>
Sensor Registered & Ready
Once probe() succeeds, the matching driver owns the device — every later registration attempt is rejected.
IMX219 Custom Driver Bring-Up
3 / 15

## Slide 4
LINUX DRIVER MODEL
Bus, Device, and Driver
The match mechanism that decides which driver owns the sensor
DEVICE
I2C address + compatible string, declared in the Device Tree
DRIVER
of_match_table plus probe() / remove() callback functions
↓
registers
↓
registers
I2C BUS
Compares every registered device's compatible string against every registered driver's of_match_table
↓
MATCH FOUND
↓
probe() Executes
The matched driver now owns the device and can talk to the sensor over I2C
IMX219 Custom Driver Bring-Up
4 / 15

## Slide 5
SYSTEM ARCHITECTURE
Raspberry Pi Camera Stack — Internal Layout
Six layers sit between an application call and the physical sensor
Application Layer — libcamera / rpicam-apps
USER SPACE
V4L2 Core (Video4Linux2 Framework)
Media Controller Framework
KERNEL SPACE
IMX219 Kernel Driver (Official — sony,imx219)
I2C Subsystem (i2c-bcm2835)
Hardware — IMX219 Sensor (I2C control + MIPI CSI-2 data)
HARDWARE
IMX219 Custom Driver Bring-Up
5 / 15

## Slide 6
DEFAULT BEHAVIOR
Why the Official Driver Wins by Default
It is configured to bind before your module ever loads
Raspberry Pi OS ships with dtoverlay=imx219 enabled out of the box
The Device Tree declares compatible = "sony,imx219"
The kernel auto-loads the official imx219.ko driver during boot
It binds the I2C address before your custom module is even inserted
Overlay Loaded
(dtoverlay=imx219)
↓
Compatible String
Matched
↓
imx219.ko Probes
First
↓
Sensor Owned — Your Probe Is Skipped
IMX219 Custom Driver Bring-Up
6 / 15

## Slide 7
OBJECTIVE
Goal: Redirect Ownership to Your Driver
Change which probe() the kernel calls — not how the kernel itself works
DEFAULT FLOW
compatible = "sony,imx219"
↓
Official imx219 driver
↓
probe() runs
↓
V4L2 → libcamera
DESIRED FLOW
compatible = "mycompany,my-imx219"
↓
myCameraDriver.ko
↓
probe() runs
↓
Direct register access
IMX219 Custom Driver Bring-Up
7 / 15

## Slide 8
BYPASS METHOD 1
Unload or Blacklist the Module
Best for fast iteration during development
Works when the official driver is built as a loadable kernel module (imx219.ko)
Quick to test, but doesn't survive a reboot unless the module is blacklisted
Good first step before committing to a Device Tree change
$ lsmod | grep imx219
$ sudo modprobe -r imx219
# Make it permanent across reboots:
$ echo "blacklist imx219" | \
sudo tee /etc/modprobe.d/blacklist-imx219.conf
$ sudo insmod myCameraDriver.ko
$ dmesg | tail -n 20
IMX219 Custom Driver Bring-Up
8 / 15

## Slide 9
BYPASS METHOD 2
Disable Auto-Detect & the Camera Overlay
Most reliable for headless or production boards
camera_auto_detect automatically loads the official overlay at boot
Editing the boot config stops the overlay from ever being applied
Survives reboots without needing a blacklist file
$ sudo nano /boot/firmware/config.txt
# Comment out or set to 0:
camera_auto_detect=0
# Remove this line if present:
# dtoverlay=imx219
# Add your own overlay:
dtoverlay=myCameraDriver
$ sudo reboot
IMX219 Custom Driver Bring-Up
9 / 15

## Slide 10
BYPASS METHOD 3 — RECOMMENDED
Custom Compatible String
The cleanest fix: the kernel never even considers the official driver
Official Device Tree Node
imx219@10 {
compatible = "sony,imx219";
reg = <0x10>;
clocks = <&cam_clk>;
...
};
Your Driver's Match Table
static const struct of_device_id
my_match[] = {
{ .compatible =
"mycompany,my-imx219" },
{ }
};
MODULE_DEVICE_TABLE(of, my_match);
Kernel now matches ONLY your driver for this node — no module unloading required
IMX219 Custom Driver Bring-Up
10 / 15

## Slide 11
VERIFICATION
Loading & Verifying the Custom Driver
Five quick checks confirm the bypass actually worked
1
sudo insmod myCameraDriver.ko
Module loads without error
2
dmesg | grep myCameraDriver
Confirms probe() actually executed
3
i2cdetect -y 1
Sensor address (0x10) responds on the bus
4
cat /sys/kernel/my_imx219/chip_id
Returns the expected IMX219 chip ID
5
ls /dev | grep video
Device node created, if V4L2 is registered
IMX219 Custom Driver Bring-Up
11 / 15

## Slide 12
DRIVER INTERNALS
What Must Be Wired Correctly
Get these right before any register read will succeed
Parameter | Why It Matters
I2C Address & Bus Number | Must match the reg property in the Device Tree exactly
Chip ID Registers (0x0000–0x0001) | First sanity check that probe() can actually talk to the silicon
MCLK / Sensor Clock Source | The IMX219 stays silent until an external clock is supplied
Reset & Power-Enable GPIOs | Sensor remains in reset until these are sequenced in the right order
Regulator / Voltage Rails | 2.8V analog, 1.8V digital, 1.2V I/O — order matters at power-up
of_match_table Compatible String | Determines whether the kernel binds your driver at all
IMX219 Custom Driver Bring-Up
12 / 15

## Slide 13
SENSOR CONTROLS
Runtime Parameters You Can Modify
What your custom driver can read, write, and expose
Exposure Time
Controls shutter speed — brighter or darker image
Analog Gain
Amplifies the signal at the sensor; more noise at high values
Digital Gain
Additional amplification applied after the ADC
Frame & Line Length
Sets FPS and the maximum allowed exposure time
Resolution & Mode
Switch between 3280×2464, 1920×1080, 1640×1232, etc.
Streaming On / Off
MODE_SELECT register — 0x00 standby, 0x01 streaming
Test Pattern Generator
Color bars or solid colors without a lens — great for debugging
Flip, Crop & Binning
Mirror the image, crop a window, or combine pixels 2×2
IMX219 Custom Driver Bring-Up
13 / 15

## Slide 14
RECOMMENDED PATH
Testing & Validation Flow
Move from raw I2C access to full V4L2 integration one step at a time
1
Read Chip ID
>
2
Read / Write a
Test Register
>
3
Toggle Streaming
(MODE_SELECT)
>
4
Expose sysfs
Controls
>
5
Migrate to V4L2
Subdev
Each step should fully succeed before moving to the next — skipping ahead makes failures much harder to diagnose.
IMX219 Custom Driver Bring-Up
14 / 15

## Slide 15
CLOSING
Key Takeaways
Driver binding is decided by Device Tree matching — not by which module loads first
Renaming the compatible string is the cleanest, most reliable bypass method
Always verify a chip-ID read and probe() success before touching V4L2 at all
Build incrementally: raw I2C access → sysfs controls → full V4L2 subdev driver
Next Step: Integrate into the V4L2 Subdev & Media Controller Framework
IMX219 Custom Driver Bring-Up
15 / 15